# Next Mini‑Goal: Bring Up Hardware Interrupts (IRQs)
This is the moment where your kernel stops being a static program and starts reacting to the world. Once IRQs work, you can:
- run timers
- schedule tasks
- handle keyboard input
- handle APIC events
- measure time
- build preemption
- build a real kernel loop
It’s the gateway to everything dynamic.
# The Path to Achieve It
Below is the exact sequence I recommend. Each step is small, testable, and builds on the last.
## 1. Install a Real IDT Entry for IRQ0 (Timer)
You already have exception stubs. Now add:
- an IRQ0 stub in assembly
- an IDT entry pointing to it
- a simple Rust/Zig handler that prints a milestone like IRQ0!
This confirms:
- IDT works
- interrupt gates work
- your stack frame layout is correct
- your higher‑half mapping is correct
- your CPU can enter and exit interrupt context safely
This is the single most important test before enabling the PIC/APIC.
## 2. Remap the PIC (8259A)
The legacy PIC fires IRQs at vectors 0–15, which overlap CPU exceptions. You remap them to 32–47.
This is a tiny piece of code:
- send ICW1–ICW4 to both PICs
- set master offset = 32
- set slave offset = 40
- unmask IRQ0 only
After this, IRQ0 will fire at vector 32.
## 3. Enable interrupts (STI) and watch IRQ0 fire
This is the magic moment.
You’ll see:
Code
IRQ0!
IRQ0!
IRQ0!
or whatever milestone you print.
This proves:
- PIC is remapped
- IDT entries are correct
- interrupt gates work
- your stack is stable
- your paging is stable under interrupt pressure
- your kernel can handle asynchronous events
This is the first time your kernel becomes “alive.”
## 4. Add a simple tick counter
Increment a global ticks variable in the IRQ0 handler.
Print it occasionally or use it to drive a heartbeat.
This gives you:
- a working time base
- a way to measure delays
- a foundation for scheduling
## 5. Replace PIC with APIC (optional but recommended)
Once PIC IRQ0 works, switching to LAPIC + IOAPIC is straightforward.
This unlocks:
- multicore
- high‑resolution timers
- proper interrupt routing
But you don’t need this immediately.
# Why this is the perfect next step
You’ve already solved the hardest early‑kernel problems:
- paging
- higher‑half
- .bss
- phys/virt
- allocator
- IDT exceptions
IRQs are the natural continuation because they:
- validate your IDT under real pressure
- validate your stack discipline
- validate your paging under asynchronous entry
- give you a heartbeat for future subsystems
- unlock everything else (scheduler, drivers, input, timers)
And each step is tiny and testable.
If you want, I can sketch the exact IRQ0 stub, the PIC remap code, and the IDT entry layout you’ll need.